Embracing Wireless Interference : Analog Network Coding
By Sachin Katti, Shyamnath Gollakota, and Dina Katabi
Shyamala Villupuram Sundararaman
University of Freiburg
Institute für Informatik
Winter Semester 2009/10

---
Over View
- Traditional Wireless Network
- What is Network Coding?
- Embracing Wireless Interference : Analog Network Coding (ANC)
- Comparing Throughput gain of ANC using transmission networks
  - Uni – Directional Transmission Network
  - Bi – Directional Transmission Network
- Implementation of Analog Network Coding
  - Modulation/Demodulation Technique
- Synchronization and Channel Status
- Future Works
- Conclusion

---
Traditional Network
- Transmits packets
  - Sender → Router → Receiver.
- Avoid Collision.
- No throughput gain.
- Best approach to improve throughput gain
  - Network Coding Approach

---
Network Coding
- Method of attaining maximum information flow in a network
    - Also allows senders to transmit packet simultaneously
  - Approaches
    - Digital Network Coding
    - Analog Network Coding
- Digital Network Coding
  - Packets are transmitted one after the other.
  - Router XORs the packets and transmit packet to their corresponding destinations.
  - Throughput gained a bit than traditional approach.

---
Analog Network Coding
- Analog Network Coding
  - Supports wireless interference.
  - Nodes are allowed to transmit packets simultaneously.
  - Collision occurs at router node.
  - Router node adds the colliding signals and transmits to their corresponding destinations.
  - Throughput gain is more comparing to traditional network and digital network coding approaches.
- Difference between digital and analog network coding
  - Analog Network Coding
    - Nodes transmits packets simultaneously.
    - Done at physical layer.
  - Digital network coding
    - Nodes transmits packets one after the other.
    - Done at data link layer

---
Illustrative Example
- Comparing throughput gain of ANC using two transmission networks
  - Uni – Directional Transmission Network
  - Bi – Directional Transmission Network

---
Uni – Directional Transmission Network
  - Traditional Network approach – hop by hop transmission
    - Needs 3 time slots.
  - Digital Network Coding
    - Cannot reduce time slot
  - Analog Network Coding
    - Allows simultaneous transmission of packets.
    - Assume synchronization of packets at node N2.
    - Node N2 stores copy of Mi sent by Node N1.
    - Mi+1 and Mi collide at node N2 – receives interfering signals ((Mi+1)⊕Mi). Stores inverse of Mi sent by node N3.
    - Cancels the interfering signals by performing
      ((Mi+1)⊕Mi)⊕ Mi-1 = (Mi+1).
    - Time slots reduced from 3 to 2 – nodes N1 and N2 transmit packets simultaneously.
    - Throughput gained 3/2 = 1.5

---
Illustrative Example
- Uni – Directional Transmission Network
  - Traditional Network Approach
    - Message M1 transmitted from source to its destination
N1
N2
N3
N4
Destination
Source
M1
M1
M1
N3
N4
N1
N2
Time Slot 1
Time Slot 2
Time Slot 3
Destination
Source

---
Illustrative Example
Analog Network Coding Approach
Time Slot 1:
Mi
N1
N2
N3
N4
Source
Destination
Time Slot 2:
Mi
Mi
Mi+1
N1
N2
N3
N4
Destination
Source

---
Bi – Directional Transmission Network
- Traditional Network Approach
  - Needs 4 time slot to deliver packet
- Digital Network Coding Approach
  - Transmits packets one after the other.
  - Router XORs the packets M1⊕M2 and forwards XORed version.
  - Transmission steps reduced from 4 to 3
  - Throughput gained 4/3 = 1.3
- Analog Network Coding Approach
  - Transmits packets simultaneously.
  - Router uses modulation/demodulation technique to deliver packets.
  - Router adds two signals and decode and forwards those signals.
  - Transmission steps reduced from 4 to 2.
  - Throughput gained 4/2 = 2

---
Illustrative Example
- Bi – Directional Transmission Network
  - Traditional Network Approach
Router
N1
N2
M1
Router
N1
N2
Time Slot 1:
M1
Router
N1
N2
Time Slot 2:
M2
Router
N1
N2
Time Slot 3:
M2
Router
N1
N2
Time Slot 4:

---
Illustrative Example
- Digital Network Coding Approach
  Router's Performance with example
  XOR operation:
    M1 = 1101; M2 = 1010
    Router = M1⊕ M2 = 0111
  At Node N1:
  M1 ⊕ (M1⊕ M2) = (M1⊕ M1) ⊕ M2
    = 0 ⊕ M2 = M2 = 1010
  At Node N2:
  M2 ⊕ (M1⊕ M2) = M1⊕ (M2⊕ M2)
          = M1⊕ 0 = M1 = 1101
M1
N1
N1
Router
Time Slot 1:
M2
N1
Router
N1
Time Slot 2:
M1⊕M2
M1⊕M2
Router
N1
N1
Time Slot 3:

---
Illustrative Example
Analog Network Coding
S (M2)
S (M1)
Router
N1
N2
Time Slot 1:
S (M1+M2)
S (M1+M2)
Router
N1
N2
Time Slot 2:

---
Implementation of ANC using Modulation/demodulation Technique
- Modulation/Demodulation Technique
  - Bi – directional transmission network
  - Modulation - Transmission of information signal and carrier signal over communication medium.
  - QPSK – Quadrature Phase Shift Keying modulation – used for implementing ANC
    - Carrier signal sent in four possible phases 0°, 90°, 180°, 270°.
    - Digit '0' - phase difference of
      0°and less.
    - Digit '1' - phase difference of
      90°and more.
    - Two bits of information is delivered
      for each time slot
Phases	Bits
0°	00
90°	01
180°	10
270°	11

---
Modulation/demodulation at Router
- Router receives sum of two simultaneous signals from N1 and N2,
    R (M) = S (M1) + S (M2)
  - = [x1cos(t) + y1sin(t)] + [x2cos(t) + y2sin(t)]
    = (x1+x2) cos (t) + (y1+y2) sin (t)
    - Two cosine waves – in-phase signal
    - Two sine waves – quadrature phase signal
            I = x1 + x2
            Q = y1 + y2

---
Treating In-Phase and Quadrature phase as digital bit streams
- Final messages are delivered in binary bits.
- Each time slot 2 bits of information is delivered.
- Router receives XORed version of in-phase and quadrature phase
    - In-Phase :
      Si (M1 + M2) = Si (M1)⊕Si (M2)
    - Quadrature Phase :
      Sq (M1 + M2) = Sq (M1)⊕Sq (M2)
- Router R (M) transmits the following signal to node N1 and node N2:
    - S(M1 + M2) = x3cos(t) + y3sin(t)

---
Modulation/demodulation at router R(M)
Modulation/demodulation at router
Demodulation at R (M)	XOR Operation / at R (M)	Nodes N1 / Receives
X1+X2	Si (M1+M2)	S (M1)
-2	0	-1
0	1	1
0	1	1
2	0	-1
In-Phase Binary Bits		Xk = 2N-1
Si (M1)	Si (M2)	X1	X2
0	0	-1	-1
0	1	-1	1
1	0	1	-1
1	1	1	1
Table 2(a) Modulation at node N1 and N2
Table 2(b) Demodulation at router R (M)

---
Problems in Sending Packets
- Problem(s)
  - Synchronization at the router
    - Signals of nodes N1 and N2 does not arrive router at the same time.
- Solution
  - Pilot symbol approach
    - Estimates synchronization of signals and channel status.
    - Inserting 64-bit length sequence at the beginning and end of each packet before transmission.

---
Synchronization of signals and Channel Status
- Synchronization of two signals
  - Assume packet size is same for N1 and N2.
  - Node N1 and N2's packet not interfered at the router simultaneously.
  - Node N1 and N2 aligns its own packet and phase difference
  - Node N1 and N2's packet matches at router
  - Router applies usual modulation/demodulation technique
Sending
Packets
Node N1's Packet
Node N2's Packet
Node N1's Signal
Node N1
receives
Node N2's Signal
Not Synchronized
Matches with Known
Bit Sequence to compute
phase difference
   Known Pilot Sequence
Decode
Node N1's decoded
        packet
Signals interfered by
Matching known packets
 with known phase
difference
Known Packet
Known phase difference

---
Future Works
- Theoretically shown the throughput gain of ANC but practically run ANC on approaches discussed above.
- ANC shown for only three-node network. Test ANC for huge network.
  - Improves Bit Error Rate in small networks.
- Check with different packet sizes – synchronization and channel status.

---
Conclusion
- Analog Network Coding proved that
  - Throughput is higher than traditional approaches and digital network coding approach.
  - Implemented ANC using modulation/demodulation technique.
  - ANC works fine in small networks.
- However, Analog Network Coding needs further research to improve the technology.

---
References
[1] S. Katti, S. Gollakota, D. Katabi, Embracing Wireless Interference: Analog Network Coding, Proceedings of the 2007 conference on Applications, technologies, architectures and protocols for computer communications; Session:Wireless, Pages: 397-408, 2007.
[2] D.N.C. Tse and G.W Wornell. Cooperative diversity in wireless networks: ecient protocols and outage behavior, IEEE Trans. Inform. Theory; Volume 50, Pages: 3062-3080, 2004.
[3] Ram Ramanathan, Challenges: a radically new architecture for next generation mobile ad hoc networks, International Conference on Mobile Computing and Networking Proceedings of the 11th annual international conference on Mobile computing and networking; Session:Challenge Papers, Pages: 132-139, 2005.
[4] Claude E. Shannon, Two-way Communication Channels, Proc. Fourth Berkeley Symp. On Math. Statist. and Prob., Vol. 1 (Univ. of Calif. Press, 1961), Pages:611-644.
[5] David Tse, Pramod Viswanath, Fundamentals of Wireless Communication, Cambridge University Press, 2005.
[6] Shengli Zhang, Soung Chang Liew, Patrick P.Lam, Hot topic: physical-layer network coding, International Conference on Mobile Computing and Networking Proceedings of the 12th annual international conference on Mobile computing and networking; Session:New Topics, Pages: 358-365, 2006.
[7] Sachin Katti, Hariharan Rahul, Wenjun Hu, Dina Katabi, Muriel Medard and Jon Crowcroft, XORs in the air: practical wireless network coding, ACM SIGCOMM Computer Communication Review, Proceedings of the 2006 conference on Applications, technologies, architectures, and protocols for computer communications Session:Coding, Pages: 243-254, 2006.

---
THANK YOU